## Slide 1: Module-04: Part-3: Functions and Arrays
CS 1714 - Intro to Programming II

## Slide 2: Arrays in Parameters
When passing arrays in as function parameters, they are passed in by pointer as the call involves passing the array variable (without the subscript operator). That is, any changes to the array within the function may affect the actual parameters in the function call.
Additionally, you also need to pass in the size of the array in the function.

## Slide 3: Arrays as Formal Parameters
There are three approaches to passing in arrays as formal parameters. All require the array and the size.
/* Approach 1: empty subscript operator. This common approach is used by our textbook. */
void myFunction(int array[], int size)
{
}
/* Approach 2: subscript operator with size, which is not needed as there is a second parameter with the size. We are unable to access that size literal in the function. */
void myFunction(int array[10], int size)
{
}

## Slide 4: Arrays as Formal Parameters (cont’d)
/* Approach 3: The array parameter is a pointer and no subscript operator is used. This is possible due to the relationship between pointers and arrays. */
void myFunction(int* array, int size)
{
}

## Slide 5: Example
Here is an example of how to call a function that expects an array. Remember that arrays are passed by reference. Any changes that we make to the array in a function could affect the actual parameters.
int foobar[] = { 3, 5, 7 };
myFunction(foobar, 3);
void myFunction(int array[], int size)
{
int i = 0;
for(i = 0; i < size; i++)
{
array[i] = -888;
}
}

## Slide 6: Protecting Arrays
To protect an array passed into a function from being changed, add const in front of the array data type in the formal parameter.
void myFunction(const int array[], int size)
{
/* you won't be able to assign anything into the array */
}

## Slide 7: 2D Arrays in Formal Parameters
To pass 2D arrays to a function, the formal parameter for the array requires at least the second dimension’s size. Since this is needed in a formal parameter, it would make sense to have both dimensions declared as #define macros. And since macros are global, you do not need to pass in separate parameters for both dimensions.
#define ROWS 3
#define COLS 2
/* Both dimensions are provided in the formal parameter */
void myFunction(int array[ROWS][COLS])
{
}

## Slide 8: 2D Arrays in Formal Parameters (cont’d)
Here is an example of only providing the second dimension’s size in the formal parameter.
In either approach, you call the function by passing only the 2D array variable.
#define ROWS 3
#define COLS 2
/* You only need the second dimension in the formal parameter */
void myFunction(int array[][COLS])
{
}
int arr[ROWS][COLS] = { { 3, 2, 1 },
{ 6, 5, 4 } };
myFunction(arr);

## Slide 9: 2D Arrays in Formal Parameters - Advanced
Remember that an array variable is a pointer to the memory location of the first item of the array. 2D arrays can be thought of as an array of arrays.
Even though we may see it as in a table format, it’s actually stored in a single contiguous space. Each row appears one after another in memory.
int arr[ROWS][COLS] = { { 3, 2, 1 },
{ 6, 5, 4 } };
3 | 2 | 1 | 6 | 5 | 4
arr
Row 0
Row 1

## Slide 10: 2D Arrays in Formal Parameters - Advanced (cont’d)
Another option for 2D arrays in formal parameters is to declare it as a pointer.
/* With this approach, you may have to include the rows and columns
as parameters if you do not have those macros declared */
void myFunction(int* array)
{
/* The only issue is that you cannot use this double subscript
operator notation: array[i][j]. Instead, it will be
treated like a one-dimensional array: array[i]. */
}
We will revisit this approach in a later module.

## Slide 11: 2D Arrays in Formal Parameters - Advanced (cont’d)
To call this function, there are two approaches:
void myFunction(int* array)
{
}
int arr[ROWS][COLS] = { { 3, 2, 1 },
{ 6, 5, 4 } };
/* pass the memory address of the first item in the 2D array */
myFunction(&arr[0][0], ROWS, COLS);
/* pass a pointer to the first row in the 2D array */
myFunction(arr[0], ROWS, COLS);

## Slide 12: 3D Arrays in Formal Parameters
Simlar to the 2D arrays, we need to pass size of all dimensions except the first (highest) dimesion.
#define DIM_A 2
#define DIM_B 2
#define DIM_C 3
/* You can skip the first (highest) dimesion.
You need to have all other dimensions. */
void myFunction(int array[][DIM_B][DIM_C])
{
}
int arr[DIM_A][DIM_B][DIM_C] = { { {1, 2, 3}, {4, 5, 6} },
{ {7, 8, 9}, {10, 11, 12} } };
myFunction(arr);